## Slide 2: Lecture 6: Address Translation
Prof. Seyed Majid Zahedi
https://ece.uwaterloo.ca/~smzahedi

## Slide 3: Outline
Virtual to physical address translation
  Base and bound
  Segmentation
  Page table
  Multi-level table
  Inverted page table

## Slide 4: Recall: OS as Illusionist and Referee
Illusion: each process has its own processor with (almost) infinite memory capacity
Physical reality: there are only few processes, memory capacity is limited
Scheduling: need to multiplex processors (done)
Memory management: need to multiplex memory (now!)

## Slide 5: Memory Management Goals
Protection: prevent processes/threads from accessing others’ private data
  Protect kernel data from user programs
  Protect programs from themselves
  Give special access permissions to different data
  Allow processes to share data (controlled overlap)
    E.g., Shared binary file between multiple processes (e.g., fork())
    E.g., Shared memory used for inter-process communication
    E.g., Memory-mapped file shared by multiple processes
    E.g., User-level system libraries
Allocation: divide available physical memory among processes/threads
  Manage memory capacity efficiently
  Avoid memory fragmentation
  Evict memory blocks to persistent storage if needed

## Slide 6: Background: Some Basics
What is 210 bytes (where one byte is abbreviated as “B”)?
  210 B = 1024B = 1KiB (for memory, 1KiB = 1024B, not 1000B)
How many bits to address each byte of 4KiB memory?
  4KiB = 4 × 1KiB = 4 × 210= 212  12 bits
How much memory can be addressed with 20 bits? 32 bits? 64 bits?
  220B = 210KiB = 1MiB (mebibyte)
  232B = 212MiB = 22GiB (gibibyte)
  264B = 234GiB = 224TiB (tebibyte) = 214PiB (pebibyte) = 24EiB (exbibyte)
k bits
Address:
Address Space:
2k “things”
For memory, “things” translates to “bytes” (8 bits)

## Slide 7: Recall: Some Terminologies
Address space: set of accessible addresses and their state
Physical memory: data storage medium
Physical addresses: addresses available on physical memory
  For 4GiB of memory: 232B ~ 4 billion addresses
Virtual addresses: addresses generated by program
  For 64-bit processor: 264 > 18 quintillion (1018) addresses

## Slide 8: Multi-step Processing of Programs
Compiler: generate object file for each source code
  Has incomplete information when compiling each source code
  Doesn't know addresses of external objects (e.g., printf routine)
  Doesn't know where in memory compiled code will go
Linkage editor: combines objects to single relocatable, executable image
  Arranges objects in program’s virtual address space
  Reorganizes code and data by changing addresses
Loader: loads image from disk into memory for execution
  Allocates memory space to executable image
  Transfers control to the beginning instruction of the program
Dynamic linker: defers linkage of shared libraries until run time
  Brings shared libraries if it’s not already in memory,
  Binds regions of program’s virtual address to shared library

## Slide 9: Recall: Virtual Address Space Layout of C Programs
Heap
Stack
#include <stdio.h>
#include <stdlib.h>
int x;
int y = 15;
int main(int argc, char *argv[]) {
int *values;
int I;
values = (int *)malloc(sizeof(int)*5);
for (i = 0; i < 5; i++)
values[i] = i;
return 0;
}
Binary Code
Initialized Data
Uninitialized Data
Command line args and environment vars
Shared library
Shared library
0x0000…0
0xFFFF…F

## Slide 10: Recall: What Happens During Program Execution?
E.g., function calls, return, branches, etc.
Execution sequence
  Fetch instruction at PC
  Decode
  Execute (possibly using registers)
  Write results to registers/memory
  PC ← Next(PC)
  Repeat
Memory
Data
PC
Decode
Instructions
ALU
Registers
Next
Data references: Memory access on load/store instructions
Instruction references:
Memory access on every instruction

## Slide 11: Uni-programming Without Protection and Translation
There is always only one program running at a time
Program always runs at same place in physical memory
  Virtual address space = physical address space
Program can access any physical address
Program is given illusion of dedicated machine by literally giving it one
0x00000000
0xFFFFFFFF
User Process
Operating
System
Valid 32-bit
Addresses

## Slide 12: Multi-programming Without Protection and Translation
To prevent address overlap between processes, loader/linker adjust addresses while programs are loaded into memory (loads, stores, jumps)
  Virtual address = physical address
Bugs in any program can cause other programs (including OS) to crash
0x00000000
0xFFFFFFFF
User Process 1
Operating
System
User Process 2
0x00020000

## Slide 13: Multiprogramming With Protection but Without Translation
Can we protect programs from each other without translation?
  Yes: use two special registers base and limit
    Prevent application from straying outside designated area
    If application tries to access an illegal address, raise exception
  During switch, kernel loads new base/limit from PCB
    User is not allowed to change base/limit registers
0x00000000
0xFFFFFFFF
User Process 1
Operating
System
User Process 2
0x00020000
base = 0x20000
limit = 0x10000

## Slide 14: Recall: Protection With Address Translation
Process 1
Virtual Address Space 1
Code 2
Code 1
Data 2
OS heap &
Stacks
Data 1
Stack 2
Stack 1
Heap 2
Heap 1
OS code
OS data
Physical Address Space
Heap
Stack
Code
Data
Process 2
Virtual Address Space 2
Heap
Stack
Code
Data
Translation Map 1
Translation Map 2

## Slide 15: Protection With Address Translation: Discussion
Upsides
  Code can be written, compiled, linked, and loaded independently
    Threads think they have unrestricted access to their entire virtual memory range
    Threads do not need to worry about memory usage of others
  OS can provide protection
    Threads cannot affect each other if they cannot see each other’s memory
  OS can allow memory sharing
    Threads’ virtual memory regions can be mapped to same physical regions
Downsides
  Address translation adds performance overhead
  Address translation needs extra hardware support
    Extra hardware consumes area and power

## Slide 16: Base and Bound (B&B) Address Translation
Code
Data
Heap
Stack
0x000…0
0x010…0
0x000…0
0xFFF…F
+
Base
Bound
Code
Data
Heap
Stack
0x100…0
0x110…0
Virtual Address
0x001…1
0x101…1
Physical Address
0x100…0
0x010…0
>
Raise Exception

## Slide 17: B&B Address Translation: Discussion
Process is given illusion of running on its own dedicated memory starting at 0x00000000
Program are mapped to continuous region of memory
Virtual addresses do not change if program is relocated to different physical memory region
CPU
Base
Bound
Virtual Address
Physical Address
Raise Exception
Memory
+
>
yes
no

## Slide 18: B&B Address Translation: Discussion (cont.)
Upsides
  OS protection and program isolation
  Low overhead address translation
Downsides
  Expandable heap?
  Expandable stack?
  Memory sharing between processes?
  Non-relative addresses – hard to move memory around
  Memory fragmentation

## Slide 19: Issues with B&B Address Translation
Missing support for inter-process memory sharing
  E.g., it’s not possible to share code segments in two processes
Fragmentation: wasted space
  External: free gaps between allocated chunks
  Internal: don’t need all memory within allocated chunks
Process 6
Process 5
Process 2
OS
Process 6
Process 5
OS
Process 6
Process 9
OS
Process 10
Process 11
Process 6
Process 5
OS
Process 9

## Slide 20: Multi-segment Address Translation
Segment map resides in processor
  Base is added to offset to generate physical address
For each contiguous segment of physical memory there is one entry
  Segment addressed by portion of virtual address
  However, could be included in instruction instead
    E.g., mov ax, es:[bx]
Seg. | Base | Bound
0 | Base 1 | Bound 1
1 | Base 2 | Bound 2
2 | Base 3 | Bound 3
3 | Base 4 | Bound 4
Memory
Seg.
Virtual Address
Offset
Segment map
>
Raise Exception
Physical Address
+

## Slide 21: Example: Multi-segment Address Translation
Offset
Seg
0
14
13
15
0x0000
0x8000
0xC000
Virtual
Address Space
Virtual Address Format
Physical
Address Space
0x4000
0x4800
Seg. ID = 0
Might
be shared
0x4000
Seg ID # | Base | Limit
0 (code) | 0x4000 | 0x0800
1 (data) | 0x4800 | 0x1400
2 (shared) | 0xF000 | 0x1000
3 (stack) | 0x0000 | 0x3000

## Slide 22: Example: Multi-segment Address Translation (cont.)
0x4000
0x0000
0x8000
0xC000
Virtual
Address Space
0x0000
Physical
Address Space
0x4000
0x4800
Seg. ID = 0
Seg. ID = 1
0x5C00
Might
be shared
Seg ID # | Base | Limit
0 (code) | 0x4000 | 0x0800
1 (data) | 0x4800 | 0x1400
2 (shared) | 0xF000 | 0x1000
3 (stack) | 0x0000 | 0x3000
Offset
Seg
0
14
13
15
Virtual Address Format

## Slide 23: Example: Multi-segment Address Translation (cont.)
0x4000
0x0000
0x8000
0xC000
Virtual
Address Space
0x0000
Physical
Address Space
0x4000
0x4800
Seg. ID = 0
Seg. ID = 1
0x5C00
0xF000
Shared with
Other Apps
Might
be shared
Space for
Other Apps
Seg ID # | Base | Limit
0 (code) | 0x4000 | 0x0800
1 (data) | 0x4800 | 0x1400
2 (shared) | 0xF000 | 0x1000
3 (stack) | 0x0000 | 0x3000
Offset
Seg
0
14
13
15
Virtual Address Format

## Slide 24: Example: Multi-segment Address Translation (cont.)
0x0240 main: la $a0, varx 0x0244 jal strlen
… …
0x0360 strlen: li $v0, 0 ;count 0x0364 loop: lb $t0, ($a0) 0x0368 beq $r0,$t0, done
… …
0x4050 varx dw 0x314159
Fetch 0x0240
  Virtual segment number? 0, offset? 0x240
  Physical address? Base: 0x4000, so physical address: 0x4240
  Fetch instruction at 0x4240, get “la $a0, varx”
  Move 0x4050 to $a0, move PC+4 to PC
Fetch 0x244, translated to physical address: 0x4244, get “jal strlen”
  Move 0x0248 to $ra (return address!), move 0x0360 to PC
Fetch 0x360, translated to physical address: 0x4360, get “li $v0, 0”
  Move 0x0000 to $v0, move PC+4 to PC
Fetch 0x0364, translated to physical address 0x4364, get “lb $t0, ($a0)”
  Since $a0 is 0x4050, try to load byte from 0x4050
  Translate 0x4050 (0100 0000 0101 0000): virtual segment #? 1, offset? 0x50
  Physical address? Base: 0x4800, physical address; 0x4850
  Load byte from 0x4850 to $t0, move PC+4 to PC
Seg ID # | Base | Limit
0 (code) | 0x4000 | 0x0800
1 (data) | 0x4800 | 0x1400
2 (shared) | 0xF000 | 0x1000
3 (stack) | 0x0000 | 0x3000

## Slide 25: Multi-segment Address Translation: Discussion
Virtual address space has holes
  It’s efficient for sparse address spaces (avoids internal fragmentation)
  If program tries to access gaps, trap to kernel (segmentation fault)
When is it OK to address outside valid range?
  This is how stack and heap grow
  E.g., stack takes segmentation fault, kernel automatically increases size of stack
What must be saved/restored on context switch?
  Segment table stored in CPU, not in memory (small)
  Might store all of processes memory in disk when switched (called swapping)
What are downsides?
  Must fit variable-sized chunks into physical memory (external fragmentation)
  Limited options for swapping to disk

## Slide 26: Paged Memory
Allocate physical memory in fixed-size chunks called pages
  Can use simple bit map to handle allocation 00110001110001101 … 110010
  Each bit represents page of physical memory 1  allocated, 0  free
Should pages be as big as our previous segments?
  No, big pages could lead to internal fragmentation
    Typically, pages are small (1-16Kib)
  Consequently, each segment needs multiple pages

## Slide 27: Page-table Address Translation
Page resides in physical memory
Contains physical page and permission for each virtual page
Offset from virtual address gets copied to physical address
  E.g., 10-bit offset ⇒ 1024-byte = 1KiB pages
Virtual page number is all remaining bits
Physical page number is copied from table into physical address
V-Page # | P-Page # | Permission | V/N
0 | 10 | R | V
1 | 5 | R/W | V
2 | 22 | - | N
. . . | . . . | . . . | . . .
V-Page #
Virtual Address
Offset
Page-table Pointer
Offset
Page-table Size
Raise Exception
>
P-Page #
Physical Address
P-Page 1
P-Page 2
P-Page 3
P-Page 4
P-Page 5
. . .
Memory

## Slide 28: Example: Page-table Address Translation with 4-byte Pages
L
K
J
I
H
G
F
E
D
C
B
A
0x00
0x04
0x08
Virtual Memory
0x00
Physical Memory
4
3
1
Page Table
0
1
2
0000 0000
0000 1000
0x06?
0000 0110
0000 1110
0x0E!
0x09?
0000 1001
0000 0101
0x05!
0000 0100
0x08
L
K
J
I
H
G
F
E
D
C
B
A
0x10
0001 0000
0x0C
0000 1100
0x04
0000 0100
Notes: What is virtual address 0x6? 1|10 = 3|2 = 0xE
What is virtual address 0x9? 10|01 = 1|1 = 0x5

## Slide 29: Page-table Entry
What is in each page-table entry (or PTE)?
  Pointer to actual page
  Permission bits: valid, read-only, read-write, write-only
Read | Write | Execute | Use Case
X | X | X | Code or data; was common, but now generally deprecated/discouraged due to security risks
X | X | - | Read-write data; very common
X | - | X | Executable code; very common
X | - | - | Read-only data; very common
- | X | X | N/A
- | X | - | Interaction with devices
- | - | X | To protect code from inspection; uncommon
- | - | - | Guard; security feature used to trap buffer overflows or other illegal accesses

## Slide 30: Permissions in Action
Demand paging (more on this later)
  Keep only active pages in memory
  Place others on disk and mark their PTEs invalid
Copy-on-write
  UNIX fork gives copy of parent address space to child
  How to do this cheaply?
    Make copy of parent’s page tables
    Mark entries in both sets of page tables as read-only
    On write, page fault happens, OS creates two copies
Zero-fill-on-demand
  New data pages must carry no information (say be zeroed)
  Mark PTEs as invalid; page fault on use gets zeroed page
  Often, OS creates zeroed pages in background

## Slide 31: Memory Sharing
V-Page # | P-Page # | Permission | V/N
0 | 10 | R | V
1 | 5 | R/W | V
2 | 22 | - | N
. . . | . . . | . . . | . . .
V-Page # | P-Page # | Permission | V/N
0 | 5 | R/W | V
1 | 15 | R | V
2 | 4 | R/W | V
. . . | . . . | . . . | . . .
V-Page #
Process A’s Virtual Address
Offset
Page-table Pointer
Offset
Physical Address
P-Page #
P-Page 1
P-Page 2
P-Page 3
P-Page 4
P-Page 5
. . .
Memory
V-Page #
Process B’s Virtual Address
Offset
Page-table Pointer
P-Page #
Physical Address
Offset

## Slide 32: Example: Updating Page Table
1111 1111
stack
heap
code
data
Virtual Memory
0000 0000
0100 0000
1000 0000
1100 0000
1111 0000
page#
offset
Physical Memory
data
code
heap
stack
0000 0000
0001 0000
0101 000
0111 000
1110 0000
11101
11100
null
null
null
null
null
null
null
null
null
null
null
10000
01111
01110
null
null
null
null
01101
01100
01011
01010
null
null
null
null
00101
00100
00011
00010
Page Table
1110 1111
11111
11110
11101
11100
11011
11010
11001
11000
10111
10110
10101
10100
10011
10010
10001
10000
01111
01110
01101
01100
01011
01010
01001
01000
00111
00110
00101
00100
00011
00010
00001
00000

## Slide 33: Example: Updating Page Table (cont.)
1111 1111
stack
heap
code
data
Virtual Memory
0000 0000
0100 0000
1000 0000
1100 0000
1110 0000
Physical Memory
data
code
heap
stack
0000 0000
0001 0000
0101 000
0111 000
1110 0000
11101
11100
null
null
null
null
null
null
null
null
null
null
null
10000
01111
01110
null
null
null
null
01101
01100
01011
01010
null
null
null
null
00101
00100
00011
00010
Page Table
11111
11110
11101
11100
11011
11010
11001
11000
10111
10110
10101
10100
10011
10010
10001
10000
01111
01110
01101
01100
01011
01010
01001
01000
00111
00110
00101
00100
00011
00010
00001
00000
What happens if stack grows to 1110 0000?

## Slide 34: Example: Updating Page Table (cont.)
1111 1111
stack
heap
code
data
Virtual Memory
0000 0000
0100 0000
1000 0000
1100 0000
1110 0000
Physical Memory
data
code
heap
stack
0000 0000
0001 0000
0101 000
0111 000
1110 0000
11101
11100
11101
11100
null
null
null
null
null
null
null
null
null
10000
01111
01110
null
null
null
null
01101
01100
01011
01010
null
null
null
null
00101
00100
00011
00010
Page Table
11111
11110
11101
11100
11011
11010
11001
11000
10111
10110
10101
10100
10011
10010
10001
10000
01111
01110
01101
01100
01011
01010
01001
01000
00111
00110
00101
00100
00011
00010
00001
00000
stack
Allocate new pages where room!
Challenge: table size equal to # of pages in virtual memory!

## Slide 35: Page-table Address Translation: Discussion
What needs to be switched on context switch?
  Page-table pointer and page-table size
How big is page table?
  32-bits and 4KiB pages ⇒ 220 entries x 4B each ⇒ 4MiB
  64-bits and 4KiB pages ⇒ 252 entries x 8B each ⇒ 32PiB
Upsides
  + Simple memory allocation
  + Easy to share
Downsides
  − Inefficient for sparse address spaces
  There are too many unused page-table entries
  What if page size is very small?
    With 1KiB pages, we need 222 (~4 million) table entries!
  What if page size is too big?
    Wastes space inside of page (internal fragmentation)

## Slide 36: Two-level Page-table Address Translation
Tables fixed size (e.g., 1024 entries)
  On context switch: save single page-table-pointer register
Valid bits on page-table entries
  Don’t need every 2nd-level table
  Even when exist, 2nd-level tables can reside on disk if not in use
10 bits
10 bits
12 bits
V-P1 Index
Virtual Address
V-P2 Index
Page-table Pointer
4 bytes
Offset
4 bytes
4K
P-Page #
Offset
Physical Address

## Slide 37: Example: Two-level Page-table Address Translation
1111 1111
stack
heap
code
data
Virtual Memory
0000 0000
0100 0000
1000 0000
1100 0000
1110 0000
Physical Memory
data
code
heap
stack
0000 0000
0001 0000
0101 000
0111 000
1110 0000
stack
111
110 null
101 null
100
011 null
010
001 null
000
11 11101
10 11100
01 10111
00 10110
11 01101
10 01100
01 01011
00 01010
11 00101
10 00100
01 00011
00 00010
11 null
10 10000
01 01111
00 01110
Page Tables
(level 2)
Page Table
(level 1)
p1#
offset
p2#

## Slide 38: Example: Two-level Page-table Address Translation (cont.)
stack
heap
code
data
Virtual Memory
1001 0000
(x90)
Physical Memory
data
code
heap
stack
0000 0000
0111 000
(0x80)
stack
111
110 null
101 null
100
011 null
010
001 null
000
11 11101
10 11100
01 10111
00 10110
11 01101
10 01100
01 01011
00 01010
11 00101
10 00100
01 00011
00 00010
11 null
10 10000
01 01111
00 01110
Page Tables
(level 2)
Page Table
(level 1)
In best case, total size of page tables number of pages used by program virtual memory. Requires two additional memory access!

## Slide 39: Multi-level Address Translation: Segments and Pages
Seg. | Base | Bound
0 | Base 1 | Bound 1
1 | Base 2 | Bound 2
2 | Base 3 | Bound 3
3 | Base 4 | Bound 4
V-Page # | P-Page # | Permission | V/N
0 | 8 | R | V
1 | 19 | R/W | V
2 | 7 | R | V
. . . | . . . | . . . | . . .
What must be saved/restored on context switch?
  Contents of top-level segment registers
Seg #
Virtual Address
Offset
Segment Map
Check Permissions
Raise Exception
V-Page #
>
Physical Address
Offset
P-Page #
Page Table

## Slide 40: Example: Multi-level Paged Segmentation (x86)
Global descriptor table (segment table)
  Pointer to page table for each segment
  Segment length
  Segment access permissions
What should be saved on context switch?
  Change global descriptor table register (GDTR, pointer to global descriptor table)
Multi-level page table
  32-bit: two-level page table (per segment)
  64-bit: four-level page table (per segment)

## Slide 41: x86 32-bit Virtual Address
4KiB pages; each level of page table fits in one page

## Slide 42: x86 64-bit Virtual Address
Fourth-level table maps 2MiB, and third level table maps 1GiB of data
If physical memory covered by fourth level table is contiguous, then one third-level entry can directly point to this region instead of pointing to fourth-level page table

## Slide 43: Example: x86 64-bit PTE
V: Valid
W: Read/write
O: Owner (user/kernel)
WT: Write-through (more on this soon)
CD: Cache-disabled (page cannot be cached)
A: Accessed: page has been accessed recently
D: Dirty bit (page has been modified recently)
L: Large page
G: Global
CP: Copy-on-write
P: Prototype PTE
U: Reserved
SW: Software (working set index)
NX: No-execute
P-Page Number
Reserved
U
L
D
A
CD
WT
O
W
V
0
1
2
3
4
5
6
7
8
39-12
51-40
SW
CW
GL
P
9
10
11
62-52
63
NX

## Slide 44: Multi-level Address Translation: Sharing Entire Segment
Seg. | Base | Bound
0 | Base 1 | Bound 1
1 | Base 2 | Bound 2
2 | Base 3 | Bound 3
3 | Base 4 | Bound 4
Seg. | Base | Bound
0 | Base 1 | Bound 1
1 | Base 2 | Bound 2
2 | Base 3 | Bound 3
3 | Base 4 | Bound 4
Seg #
Process A’s Virtual Address
Offset
Segment Map
Page #
Seg #
Process B’s Virtual Address
Offset
Segment Map
Page #
V-Page # | P-Page # | Permission | V/N
0 | 8 | R | V
1 | 19 | R/W | V
2 | 7 | R | V
. . . | . . . | . . . | . . .

## Slide 45: Aside: Shared Library Address Space
Shared library’s global and static variables are private to each process
  Each process has read and write permissions on its own copy of variables
Shared library’s code is shared between different processes
  Each process only has read and execute permissions on shared code
Shared library code must be position-independent code (PIC)
  Same library code could be mapped to different virtual address regions in different processes
  Code must execute properly regardless of its absolute virtual address
  Code cannot contain absolute virtual addresses for data and instruction references
Data references are made indirectly through global-offset tables (GOT)
  GOT is located at fixed offset from code and can be accessed using PC-relative offset
  GOT has one entry per variable which contains absolute address of that variable
  GOT is private to each process, and processes have read and write permissions to their GOT
Similarly, instruction references are made indirectly through procedure-linkage table (PLT)

## Slide 46: Multi-level Address Translation: Discussion
+ Allocate only as many page-table entries as needed for application
  In other words, sparse address spaces are easy
+ Easy memory allocation
  Bit-map memory allocation
+ Easy sharing
  Share at segment or page level (need additional reference counting)
− One extra pointer per page
  One pointer per 4 -16KiB pages
− Page tables need to be contiguous
  However, we can make each table to fit exactly into one page
− Two (or more, if > 2 levels) lookups per reference
  Seems very expensive!

## Slide 47: Inverted Page Table
In all previous methods (forward page tables), size of page table is at least as large as amount of virtual memory allocated to processes
  Physical memory may be much smaller
Inverted page table fixes this problem by using hash table
  Size of hash table is related to size of physical memory not virtual address space
  Very attractive option for 64-bit address spaces (e.g., PowerPC, UltraSPARC, IA64)
Notice any downsides?
  Complexity of managing hash chains: often in hardware!
  Poor cache locality of page table
Offset
V-Page #
Virtual Address
Hash
Table
Offset
P-Page #

## Slide 48: Inverted Paging Example (cont.)
11101
11100
10111
10110
10000
01111
01110
01101
01100
01011
01010
00101
00100
00011
00010
1111 1111
Virtual Memory
0000 0000
0100 0000
1000 0000
1110 0000
Physical Memory
data
code
heap
stack
0000 0000
0001 0000
0101 000
0111 000
1110 0000
Inverted Table
Hash(v-page#) = p-page#
stack
h(11111)=
h(11110)=
h(11101)=
h(11100)=
h(10010)=
h(10001)=
h(10000)=
h(01011)=
h(01010)=
h(01001)=
h(01000)=
h(00011)=
h(00010)=
h(00001)=
h(00000)=
stack
heap
code
data
Total size of page table number of pages used by program in physical memory

## Slide 49: HW vs. SW Address Translation
Does kernel require HW support for translation?
  No! Almost anything that can be done in HW can also be done in SW (might end up being too expensive, but possible!)
Implement page tables in HW
  All memory reference pass through memory management unit (MMU)
  MMU generates page fault if it encounters invalid PTE
  Fault handler will decide what to do (more on this later)
  + Relatively fast (but still many memory accesses!)
  − Inflexible, complex hardware
Implement page tables in SW
  + Very flexible
  − Every translation must invoke fault!
In fact, we need a way to cache translations for either case

## Slide 50: Address Translation Comparison
Method | Advantages | Disadvantages
Segmentation | Fast context switching: Segment mapping maintained by CPU | External fragmentation
Page-table translation | No external fragmentation, fast easy allocation | Large table size ~ virtual memory
Multi-level translation | Table size ~ # of pages in virtual memory, fast easy allocation | Multiple memory references per page access
Inverted table | Table size ~ # of pages in physical memory | Hash function more complex

## Slide 51: Summary
Segmentation
  Segment ID associated with each access
  Each segment contains base and limit information
Page tables
  Memory divided into fixed-sized chunks of memory
  Virtual page # from virtual address mapped through page table to physical page #
Multi-level tables
  Virtual address mapped to series of tables
  Permit sparse population of address space
Inverted page table
  Use of hash-table to hold translation entries
  Size of page table ~ size of physical memory rather than size of virtual memory

## Slide 52: Questions?
globaldigitalcitizen.org

## Slide 53: Acknowledgment
Slides by courtesy of Anderson, Ousterhout, Culler, Stoica, Silberschatz, Joseph, and Canny